## Slide 1: Workload-aware Storage
CSE791 Course presentation
Qiuwen Chen

## Slide 2: Outline
Problem definition
f4: Facebook’s Warm BLOB Storage System
Pelican: A Building Block for Exascale Cold Data Storage
  Focus
  Approach
  Evaluation
Conclusion

## Slide 3: Problem definition
BLOB (Binary Large OBjects)
  Immutable: once written, seldom modified
  Unstructured: no uniform format
  Diverse: size, life cycle, access pattern
  A lot of them

## Slide 4: Problem definition
Data cool off – use different infrastructure

## Slide 5: Problem definition
Hot data
  Haystack
3.6X

## Slide 6: Warm data
f4: Facebook’s Warm BLOB Storage System

## Slide 7: Goals
Storage space efficiency
Error detection & correction
Cell
  Storage & compute
  Reside in a datacenter

## Slide 8: Data placement and error correction
Reed-Solomon (10, 4), rate 1.4x
Tolerate 4 racks failure

## Slide 9: Read operation
Index read -> data read
Cell local failure

## Slide 10: Datacenter failure
Duplication
  1.4 * 2 = 2.8x
XOR encoding
  1.4 * 3 / 2 = 2.1x

## Slide 11: Comparison

## Slide 12: Evaluation
Hot and warm
  Two week sample from the router tier of 0.1% of reads

## Slide 13: Evaluation
Workload
  Peak at 8.5 IOPS/TB < 20 (Maximum rate of f4)

## Slide 14: Evaluation
Latency
  Sufficiently good

## Slide 15: Cold data
Pelican: A building block for exascale cold data storage

## Slide 16: Goals
Achieve right-provisioning (vs. full-provisioning) in rack level
  At most 8% of disks spun up
  Not only subject to failure domain, but also power and cooling
  Hard, soft
Data placement
IO scheduling

## Slide 17: Setup
Rack -> tray -> disks
  2 disk spun up per tray
  1 disk spun up per vertical array

## Slide 18: Data placement
Random placement O(n2)
Maximizing concurrency O(n)
  Groups
  Fully conflicting
  Fully independent

## Slide 19: Data placement
Error correction
  RS(15, 3) -> 18 disks for 1 blob
  Rump up to 24 disks per group (4 sets, find the top 3 available ones)
Assignments
  12 fully conflicted groups -> class
  4 independent class -> 6 racks
  48 groups of 24 disks

## Slide 20: IO scheduling
4 independent scheduler for each class
One group out of 12 can be active
Naïve approach
  Group activation: 14.2 sec
  High latency
Request batching
  Re-order limitation u
  u – tradeoff between fairness and throughput
  Two queue for client and rebuilt traffics

## Slide 21: Simulator
Model
  Poisson arrivals of 1GB blobs
Cross validation

## Slide 22: Evaluation
Throughput

## Slide 23: Evaluation
Time to first byte

## Slide 24: Evaluation
Power consumption

## Slide 25: Conclusion
Production level system design for storing less frequently accessed data
Characterizing Storage Workloads with Counter Stacks
  Data placement over storage architectures
  Approximate algorithm to estimate the MSR (miss ratio curve)
Improvement
  Use sophisticated soft encode schemes
    Turbo, LDPC, etc